Tutorial

This tutorial is meant to be a general guide to functionality - the intention is not to cover all functionality but expose the user to various tools for further exploration. Additional documentation can be found by navigating the Contents. Clicking a link will navigate you directly to the help topic, which provides detailed information on the use and functionality of the components of the application.

If you are new to the system, Create new account, otherwise, log in.

- If you have forgotten your password, Request new password.

- To update your account settings, including Password, edit My Account.

- Click the Map menu to navigate to the map.

- Familiarize yourself with the Map Navigation.

- Use the Find address or place tool  to find Roaring River State Park.

- Using the Zoom to Coordinates or Scale tool , zoom in to a Scale of 1:18,056.

- Add a Spatial Bookmark for Roaring River State Park.

- Zoom to the Default Extent  of the map.

- Perform a Feature Search using the Resource: Cities to find NAME: Hannibal (Mark Twain's hometown) and Zoom to it.

- Add a Spatial Bookmark for Hannibal.

- Using the newly created Spatial Bookmark, zoom to Roaring River State Park.

- Alter the content of the map:

- Switch Basemap  to USA Topo Maps to determine where campsites and picnic areas are located within the state park.

- Using the Zoom to Coordinates or Scale tool , zoom out to a Scale of 1:144,448.

- Switch Basemap  to Light Gray Canvas.

- Work with the Layers to make them visible/invisible, view their symbology, alter the layer transparency,...

- Use the Add Resource tool  to add a map service to the map via URL: http://msdisweb.missouri.edu/arcgis/rest/services/LC_JourneyBegins_BETA/MapServer and name it Lewis & Clark Journey.

- The Lewis & Clark Journey map service is added within the Added Resources section of the Layers tab.

- Hover over the Lewis & Clark Journey layer name and click the dropdown  icon to the right and select Zoom To to zoom to the extent of the layer.

- Using the Zoom to Coordinates or Scale tool , zoom to Latitude/Longitude (Decimal) coordinates of Latitude: 39.220268 and Longitude: -93.536797 at a Scale of 1:144,448.

- Utilize the Identify  tool to view various notes regarding the Lewis & Clark Journey at this location.

- Make a Map by adding Points, Lines, Polygons and/or Text to the map.

- Add a Point by:

- digitizing a point using the default Draw Shape tool .

- entering Coordinates  via the Additional Mapping Options tool .

- Add a Polygon by:

- digitizing a polygon using the default Draw Shape tool .

- uploading a shape from a file (shapefile, KML, GML) using the Upload Shapes  tool.

- Add a Line by:

- digitizing a line after selecting the Use Freehand option from Draw Settings .

- Add Text to the map of various colors, sizes, and styles.

- Edit Annotations  to edit the Line to change the Line Style, Line Color, and Line Thickness.

- After Making a map by adding various annotations, Print  the map.

- Create Project to submit for environmental review. Consider doing so via one of the following multiple options:

- Draw shape

- Upload shape from a (zipped) shapefile

- Additional Mapping Options, including:

- Map Layers:

- Select the Cities boundary identified by the Feature Search performed in Step 3

- Make a Map drawn in Step 7

- Coordinates - Latitude/Longitude (Decimal) with Latitude (Northing) of 39.220268 and Longitude (Easting) of -93.536797

- Drawing a point or line feature(s)

- Edit Project:

- Edit the project details.

- Edit the spatial boundary of the project. Note that this enables the user to edit the project details as well.

- Clear All Annotations from the map.

- View Project for the project created to download and review the Report File and Boundary Shapefile, in the case where the Review Status reflects Report Generated.

- Log out to close your session.

back to top

How To...

Log In

Log In

- Log Out

- Edit My Account

- Request new password

Map

Alter the map display

Switch Basemap

- Add Resources (a.k.a add map service)

- Layers - make visible/invisible

- Make A Map - add features and labels to the map

- Draw/Edit

Navigation and map tools

Identify a feature

- Feature Search (a.k.a. find something on the map)

- Find Address or Place

- Map Navigation

- Measure

- Overview Map

- Print

- Spatial Bookmarks - create, use and edit

- Zoom To Coordinates or Scale

Create Project

Create Project for environmental review

- Draw/Edit

My Projects

My Projects

Create New Account

Steps:

Within the Home page, click Create New Account. Alternatively, click Register in the top right corner of any page.

- Within the User account page, supply the required information (denoted by red asterisks *).

- Once the form is filled out, read and Accept Terms & Conditions of Use .

- Click Create new account  at the bottom of the page.

- A message is displayed on the Home page, indicating that further instructions have been sent to the email address entered during account creation. This verifies that the email address is valid and minimizes spam submissions.

- Open the email and click on the link provided to activate the new account.

- Within the Reset password page, click the Log in  button.

- Create a new password and confirm it.

- If desired, upload a picture and set the locale Time zone.

- Click Save at the bottom of the form.

- A message will appear at the top of the page indicating the changes have been saved; the new account is now enabled.

- Proceed to the desired menu to begin working.

back to top

Related Topics

Log In

- Log Out

- My account

- Request new password

Log In

Steps:

Within the Home page, enter your E-mail and Password.

- Click the Log in  button.

- Once logged in, proceed to the desired menu to begin working.

back to top

Related Topics

Create new account

- Log Out

- My account

- Request new password

Log Out

Steps:

From any page, click Log out in the upper right corner.

- You will be returned to the Home page.

Related Topics

Create new account

- Log In

- My account

- Request new password

My Account

Allows user to update account settings, including Password.

Steps:

From any page, click My account in the upper right corner.

- Within your account page, click the Edit  button to modify your user settings.

- To change the E-mail address or Password associated with the account, enter the Current Password.

- NOTE: If you have forgotten your password, click Request new password under the Current password text box.

- Click Save  at the bottom of the form.

- A message will appear at the top of the page indicating the changes have been saved; the new account is now enabled.

- Proceed to the desired menu to begin working.

back to top

Related Topics

Create new account

- Log in

- Log out

- Request new password

Request new password

Steps:

Within the Home page, click Request new password.

- In the User account page, enter the E-mail associated with your account and click E-mail new password .

- A message will be displayed indicating that further instructions have been sent to the e-mail address entered.

- Open the email and click on the link provided to activate the new account.

- Within the Reset password page, click the Log in button.

- Create a new password and confirm it.

- If desired, upload a picture and set the locale Time zone.

- Click Save  at the bottom of the form.

- A message will appear at the top of the page indicating the changes have been saved; the new account is now enabled.

- Proceed to the desired menu to begin working.

back to top

Related Topics

Create new account

- Log In

- Log out

- My account

Map

The tabs within the Map can be minimized by clicking the Close Pane  icon to the right of the tabs. To display the tabs, click the Open Pane  icon. The active tab, or the tab currently in use at any given time, is shown in white.

The Map includes options to:

                - Switch Basemap

                - Add Resources

                - Create a Project

                - Alter Layers

                - Make a Map

                - Perform a Feature Search

Add Resources

Content can be added to the map viewer from:

a map service (via its URL)

- File (current file type only includes shapefile)

Steps:

Within the map, click the Add Resources  button, located in the upper left corner of the map title bar.

- The resulting Add Resource dialog provides options to add resources to the map, either a map service via its URL or a shapeFile.

back to top

URL:

Both Map Services and Image Services published on ArcGIS Online, on GIS servers that are available on a local machine or network, or from servers publicly available on the Internet are available for use. Cached services must be in the WGS 84 Web Mercator (Auxiliary Sphere) projection, because ArcGIS Server cannot reproject cached services, and use the standard scale levels supported by Google, Bing, and ESRI's arcgis.com. To test the map service prior to adding it to the map viewer, see the Test Map Service help topic.

NOTE: Cached map services published through ArcGIS Online do not support all of the capabilities of cached map services published through ArcGIS Server. Since the underlying data is not retained, the Identify tool is not supported.

On the Add Resource dialog, select the URL radio button, if not already selected.

- Enter the  URL of Mapservice to Add (i.e., http://services.nationalmap.gov/ArcGIS/rest/services/USGSTopoLarge/MapServer).

- Enter a Unique Title for Resource.

- Click Add Mapservice  button to add the service to the map.

- NOTE: If the map service is not protected, the following prompt will be displayed. Click Yes to continue.

- NOTE: If the map service does not successfully add to the map (i.e. the spinner spins endlessly and the map service is not added to the map viewer or a Register Layer Failed: RequestTimeout error is received, consult the Test Map Service help topic.

back to top

File:

Current functionality only allows for shapefiles to be added. The shapefile, including all component files, must be zipped into a zip file with no additional directories or files. A valid .prj file must be included in the zip file. Maximum file size not to exceed 2 GB.

On the Add Resource dialog select the File radio button, if not already selected.

- Enter a Unique Title for Resource.

- Click Select File to Upload button  and navigate to the file containing the layer to add to the map viewer.

- If the uploaded zip file does not contain all components of the shapefile, including a valid .prj file, the following error will be displayed:

back to top

- To remove a map service from the map, click on the dropdown  icon to the right of the resource in the Map Resources dialog and choose Remove.

back to top

Related Topics:

Feature Search

- Map Resources

- Map Services

- Test Map Service

- Using Insecure Map Services

Map Services

The following overview of map services includes some things to keep in mind when investigating map services published by you or others, that you may wish to add.

Projection

- Cached Map Services

- Dynamic Map Services

- Comparison: Cached vs. Dynamic Map Services

Projection

The Map displays data using the WGS_1984_Web_Mercator_Auxiliary_Sphere (EPSG code/spatial reference ID 3857) projection, which is the map projection used by most online basemap services, including ArcGIS, Bing, and Google. Any map services that will be displayed as reference layers must be capable of being displayed in this projection. Dynamic ArcGIS map services can be reprojected on-the-fly; however, this does negatively impact performance. Performance will be best if you use map services published in the Web Mercator projection. Cached map services are typically only available in the projection in which they were cached.

back to top

Cached Map Services

The best way to create fast map services is to cache them. With a cached map service, the server draws the map at a set of predefined scale levels and saves the images. When the server receives a request for a map, it's much quicker to return one of these cached images than to draw the map again. Caching is appropriate for basemaps and maps that don't change often.

Benefit:

- improved performance

- Limitation:

- does not allow filtering

- does not allow layer visibility to be altered (ie. can’t be turned on or off)

- Cached map services published from ArcGIS Online will not be available with the Filter, Identify, or Feature Search tools.

- Projection: Must use same projection as basemaps – ArcGIS Server cannot reproject cached services.

- WGS 84 Web Mercator (Auxiliary Sphere) projection enables the map services to be used in conjunction with any of the major online base maps (Esri, Bing, Google).

- Cached services in the WGS 84 Web Mercator (Auxiliary Sphere) projection will provide the best performance

- Cached maps must use the standard scale levels supported by Google, Bing, and ESRI's arcgis.com.

- If cached services are in a different projection, they can be created as dynamic services, which will allow them to be reprojected; however, we don't know enough about the underlying data sets to know what performance will be like. It's possible that this won't be sufficient, and you'll still need to provide cached services in the target projection.

- It is not necessary to reproject all of the individual layers but just alter the projection of the map documents. Then republish the map documents as a second service (second to what you’re using for your purposes), and build the cache.

back to top

Dynamic map services

Layers published as dynamic map services can be rescaled and re-projected on the fly.

Benefit:

- Allows filtering

- Allows layer visibility to be altered (ie. can be turned on or off)

- Limitation:

- Decreased performance because needs to draw map on the fly

- Projection: any projection for which there is a built-in Esri transformation from the source projection to the target projection. This can be verified through ArcMap - if ArcMap can handle it, it should be fine. Performance will be better, though, if the source projection already matches the target projection.

- Operations Allowed: when publishing the map service, indicate Map, Query, and Data as Operations Allowed or not all the tools indicated below will be available for use with the map service.

back to top

Comparison: Cached vs. Dynamic map services

back to top

Related Topics:

Add Resources

- Test Map Service

- Using Insecure Map Services

Test Map Service

Prior to adding a map service, test the map service to verify it functions. If the map service is not functioning, it will not work in Arizona Environmental Review Tool.

Indications that the map service may not be functioning include:

the spinner spinning non-stop and the map service never adding to the map viewer

- the following type of error is received: Register Layer Failed: RequestTimeoutError... This error indicates that the map service is not available.

Steps:

Copy the URL of the map service into a web browser. If an error, such as that shown below, is received the map service is not functioning correctly - contact the host of the map service to resolve it. In this state, the map service will not work within Arizona Environmental Review Tool.

- If you connect to the map service details successfully (as shown below), then the map service exists.

- Within the map service details window (shown above) of the ArcGIS Rest Services Directory, click the ArcGIS.com Map link to verify that the map service is functional in the ArcGIS.com Map. If it does not work in the ArcGIS.com Map, it will not work in Arizona Environmental Review Tool.

- NOTE: You may need to log in to ArcGIS.com to view the map service.

- Once successfully tested in the ArcGIS.com Map, as shown above, add the map service to the Biotics 5 map viewer via the Add Resource tool.

back to top

Related Topics:

Add Resources

- Map Services

- Using Insecure Map Services

Using Insecure Map Services

The URL you have provided is to a map service not protected by SSL and you should first try adding this URL with the 'https:' prefix instead of 'http:'. If you continue to add an insecure service, it may be blocked by the browser. If not blocked, the browser will treat this page as insecure, and give a warning.

Google Chrome

- Firefox

- Internet Explorer

Google Chrome

Chrome opens a very subtle shield icon, shown in the screenshot below, when attempting to add a map service to the map. At first glance the user may mistake this for the map viewer not working properly when it's the actually due to the way the browser treats insecure map services.

To load the map service, click the shield  icon, which displays a second message.

- Within the message indicating that the page includes scrip from unauthenticated sources. click the link to Load unsafe script.

- In the subsequent Confirm Reload dialog, click Reload this Page. This will reload the map viewer page in a mode that allows mixed content to be used. This has the unfortunate side effect of clearing out what has been previously done in the map viewer, so the map service will need to be added again.

This time the map service is added, but the URL bar shows a warning that the page contains insecure content. This warning continues to be present if the user navigates away from the map viewer to other pages or open up the full record pages in new windows.

The browser only performs these behaviors for the first map service that's added insecurely, and the warning message will indicate what needs to be done. No further warnings or prompts will be given upon adding subsequent insecure map services.

back to top

Firefox

Click the small gray and white shield icon at the far left of the URL box near the top of the browser window.

- Within the dialog which opens upon clicking the shield, select Disable Protection on This Page.

- Then, click Leave Page to allow the page to load again with the map resources enabled.

NOTE: You will have to do this every time you open the Map Viewer, even in the same Biotics session.

back to top

Internet Explorer

From the Tools menu, select Internet Options.

- Within the Internet Options dialog, on the Security tab, select the Trusted sites zone and click the Sites button.

- Add all web domains generating this error message to the Trusted Sites list, including *.natureserve.org. WARNING: don't do this with domains you don't trust or are not sure about.

- Close the Trusted sites dialog.

- Back in the Internet Options dialog, still in the Security tab, with the Trusted sites zone selected, click the Custom Level button.

- Within the Security Settings - Trusted Sites Zone dialog, scroll down to the Miscellaneous options (almost half way down), and set the Display mixed content to Enable.

- Click OK to save changes within the Security Settings - Trusted Sites Zone dialog.

- Click OK to save changes within the Internet Options dialog.

- Exit and re-start Internet Explorer.

NOTE: this setting allows IE to display content using both https and http protocols in a mixed environment, and should only be used with trusted web domains. Malicious content from unsecured (http) domains could potentially compromise data from secure (https) domains with which it is mixed

back to top

Related Topics:

Add Resources

Feature Search

The Feature Search tool provides the ability to identify features in a layer, including those added to the Map via the Add Resources tool, according to criteria specified by a query.

Once a search has been completed, the search criteria is saved for your convenience. Therefore, the next time the Feature Search tab is opened, the previously used search criteria still applies. If you want to define a new search, click Reset .

NOTE: The Feature Search option is not available for cached map services published from ArcGIS Online because such services do not support all of the capabilities of those published through ArcGIS Server.

Search for a feature based on:

Attribute Search

- Spatial Search

- or a combination thereof

Steps:

Within the Map, navigate to the Feature Search tab.

- In the Feature Search tab, select the Resource, the layer on which the search is to be performed, from the dropdown menu.

- The layer will automatically be displayed and the Resource Visibility checkbox indicated. NOTE: If the default Resource is the desired layer, manually indicate the Resource Visibility checkbox to display the layer.

- Define search criteria according to an Attribute Search and/or designating a location in which to perform a Spatial Search.

- To clear the defined expression, click the Reset  button.

- NOTE: A green check mark  icon on a section indicates that criteria have been defined within that section of the Feature Search tab.

Attribute Search:

The fields in the Attributes section differ according to the layer specified in Resource dropdown.

If not already expanded, click the Attributes label to expand the section.

- Define the search criteria by selecting a value(s) from the various field dropdown menus.

- Select multiple values by holding down the SHIFT key and selecting the values

- Select specific values by depressing the CTRL key and selecting the values.

Spatial Search:

The Spatial Search enables selection of Resource features based on their location in relation to the selected features defined within Search By; in an ad-hoc manner.

Click Spatial Search to expand the accordion section.

- From the Search By dropdown, select how the search area will be defined.

- Box, Polygon, Point, or Line - digitize the search area according to the tooltip instructions.

- To re-define the search area, click the Select by Drawing  button to digitize the search area.

- Features from map resource:

- From the Resource dropdown menu, select the layer from which to copy the shape(s).

- NOTE: If the chosen Resource is comprised of multiple layers, an additional Layer dropdown list will be displayed from which to select the given layer to copy the shape(s).

- Click theSelect From Resource button.

- Holding the mouse button down, draw a box on the map to select the features within the layer.

- The Details dialog of the selected features will be displayed. To remove a feature from the selection, within the Details dialog, from the Tasks menu select Remove from Include List.

- The number of features selected will display in the Spatial Search section to the right of Select From Resource.

- To display the Details dialog of the selected features again, click the View  button.

- Indicate Use Buffer to buffer the selected spatial feature(s). Enter the desired buffer distance and select the distance unit from the dropdown. A graphic will display the buffered area.

- NOTE: A positive distance will buffer outside the feature whereas a negative distance will buffer within the feature. Negative distances cannot exceed the size of the shape, nor can they be used with Point or Line features. The following error will be displayed when the negative distance exceeds the size of the shape.

- From the Search Type dropdown, define how features within the Resource will be selected by the shape(s) specified within the Spatial Search:

- Intersects - selects features from the Resource which are crossed by or are contained within the search selection

- Contains - selects features from the Resource which are completely contained by the search selection (nothing outside the search selection).

- Within - selects features from the Resource which the search selection falls entirely within (nothing outside the Resource shape).

- Touches - selects features from the Resource which the search selection touches, even by sharing a border or vertex.

- To clear the spatial graphic representing the search area, uncheck the Show Spatial Graphic  checkbox.

Results

Click Search  to run the search based on the defined criteria.

- The search results will be displayed within the Results accordion section at the bottom of the Feature Search tab.

- The Results section provides the following functionality, which will be applied to selected records. Select/deselect records by checking/unchecking individual records. Alternatively, select/deselect all records within a level of the tree by checking/unchecking the higher level entry.

- Table - displays the results within a table format. In addition to the same Zoom and Flash functionality below, the table format also enables the user to Print to PDF and Export as CSV.

- Details – to view the Details dialog of the indicated feature(s).

- Zoom to indicated feature(s)

- Flash indicated feature(s)

- NOTE: The search criteria is saved, for your convenience. Therefore, the next time the Feature Search tab is opened, the previously used search criteria still applies. If you want to define a new search, click Reset .

back to top

Related Topics:

Add Resources

- Details

Identify

The Identify tool is used to display the details of the geographic feature(s) or place(s) selected in the Map.

NOTE: The Identify tool cannot be used with cached map services published from ArcGIS Online because such services do not support all of the capabilities of those published through ArcGIS Server.

Steps:

Within the Map, click the  icon located in the upper right corner of the map title bar.

- Within the Identify dialog,

- Select a resource: Select to Identify Visible Resources or a specific resource from the dropdown list. If a specific resource is selected, it will be displayed on the map if it was not previously visible.
NOTE: Cached map services published from ArcGIS Online will not be available within the dropdown list because such services do not support all of the capabilities of those published through ArcGIS Server.

- Identify On: indicate whether the Identify should be applied to All Layers in Resource, Visible Layers in Resource, or Top Visible Layer in Resource. NOTE: Results will only differ when a Resource contains multiple layers.

- Identify By: select means (Point, Box, Polygon, Line) of indicating the area to identify

- Use Freehand: provides the ability to digitize a Polygon or Line feature freehand rather than by clicking to add individual vertices.

- Use Buffer: indicate to apply a buffer to the location of interest. Enter the desired buffer distance and select the distance unit from the dropdown. A dashed-line graphic will illustrate the buffered area utilized for Identifying.
NOTE: A positive distance will buffer outside the feature whereas a negative distance will buffer within the feature. Negative distances cannot exceed the size of the shape, nor can they be used with Point or Line features. The following error will be displayed when the negative distance exceeds the size of the shape.

- Show Identify Graphic: indicate to display the spatial feature utilized to demarcate the identifiable area. Uncheck to clear the spatial graphic representing the search area.

- Click on the feature/location to be identified.

- The Details dialog displays attributes of the target feature(s). A red callout points to the specific feature, highlighted in turquoise.

back to top

Related Topics:

Details

Layers

Within the Layers tab of the map, layers are segregated into accordion sections. These accordion sections can be contracted by clicking the  button or expanded by clicking the  button. Individual layers can be made visible/invisible, their symbology displayed, transparency altered, zoomed to, and details viewed.

Steps:

Within the Map, navigate to the Layers tab, if not already there.

- Make a layer visible/invisible by clicking the checkbox left of its name.

- NOTE: Certain layers are only visible at certain map scales. If a map is not available at a given map scale, the layer will be grayed out. To determine the minimum and maximum scale at which a scale will be displayed, View Details.

- Click the  icon to expand a layer to view its symbology.

- Collapse the layer by clicking the  icon.

- Hover over a layer name and click the dropdown  icon to the right to view the tasks available for the layer.

- Transparency – allows the transparency of the layer to be adjusted by sliding the indicator along the bar.

- Zoom To – zooms to the full extent of the layer.

- Remove - removes the layer from the map. NOTE: this option is only available for layers added by the user.

- View Details – opens the details for the layer within the ArcGIS Services Directory. If a secured service, a user name and password will be required to view the information. See the Min Scale and Max Scale values to determine a layers scale dependency.

- View Description - if information has been configured within the Layer Description section of the Layer, the description (metadata) will be displayed in the Layer Description dialog.

back to top

Related Topics:

Add Resources

- Switch Basemaps

- Layer

Details

The Details dialog displays the results of the Identify and Feature Search tools, and indicates the feature associated with each dialog by highlighting and pointing with a red call-out.

Zoom to feature

- Flash feature

- Navigate between features using Details dialogs, if more than one, by:

- Stepping backward or forward  through the set of dialogs

- Selecting the desired feature dialog from the dropdown list

- Show Table menu allows the Results to be displayed within a table format. In addition to the same Zoom and Flash functionality above, the table format also enables the user to Print to PDF and Export as CSV.

- Tasks menu - displays in conjunction with the Draw/Edit toolbar.

- Remove from Include List - removes the selected feature from the list.

back to top

Related Topics:

Draw/Edit toolbar

- Feature Search

- Identify

Filter

The Filter tool is available for specific layers. A filter can be applied to individual layers (with the exception of cached map services published from ArcGIS Online) in order to limit the features displayed on the map to those that meet the filter definition/criteria. More specific details on how to develop queries that define filter criteria (e.g., querying numbers, combining expressions, using nulls), are provided in the Build a Query topic.

Create Filter

- Modify or Remove Filter

- NOTE: The Filter option is not available for cached map services published from ArcGIS Online because such services do not support all of the capabilities of those published through ArcGIS Server.

Create a Filter

Within the Layers tab of the Map, click the dropdown  icon to the right of the service to be filtered and choose Filter from the available options.

- NOTE: The Filter option is not available with cached map services, only dynamic services.

- If the Resource contains multiple layers, a dropdown identifying the layers will be displayed.  Select the layer to be filtered from the Layer dropdown list.

- NOTE: If the Resource contains only a single layer, the Layer dropdown will not be displayed.

Select the attribute to use in the query from the Attribute dropdown, and then click Select.

- Click an operator (=, <>,..)

- To see a list of values for the attribute, click Get Unique Values . Double-click one of the values or alternatively, type an expression directly into the query field.

- NOTE: If Get Unique Values returns no records for lack of data in the attribute, a message will be displayed to indicate that No unique values were found for this attribute.

- NOTE: If Get Unique Values is used on a layer with many records, the following message is likely to be displayed. Respond Yes to continue or No to cancel the search for unique values.

Click Apply to apply the filter and keep the Filter dialog open or click OK to apply the filter and close the Filter dialog.

- NOTE: If there is a typographical error, or the filter has been improperly defined (i.e., ‘Vascular plant’ instead of ‘Vascular Plant’), no records will be displayed.

- The number of records resulting from the Filter will be reported.

- Within the Map Resources dialog, (Filtered) will be displayed next to the service name to indicate that the service has been filtered.

back to top

Modify or Remove Filter

To change or remove a filter, in the Layers tab, click the dropdown  icon to the right of the layer that is filtered, and choose Filter from the available options.

To remove the filter, click the Clear Attribute Filter Parameters  icon in the Filter dialog.

  - To modify any part of the filter expression:

  - Place the cursor within the sequence and use either the <Delete> or <Backspace> keys to remove the desired part(s).

  - Click Apply to apply the revised filter and keep the Filter dialog open, or click OK to apply the filter and close the Filter dialog.

back to top

Related Topics:

Build a Query

Build a Query

A query enables the identification of records that meet criteria specified for selected attribute(s) of a resource (layer).

Strings

- Wildcard Characters

- Null values

- Querying numbers

- Calculations

- Operator precedence

- Combining expressions

- Querying dates

Strings

Strings must always be enclosed within single quotes. For example:

PC_NAME_EN = 'Ivvavik National Park of Canada'

Strings in expressions are case sensitive. To make a case insensitive SQL search, an UPPER or LOWER function can be used to convert all values to the same case. For example, the following expression will select managed area names stored as either BIRD ISLANDS SANCTUARY or Bird Islands Sanctuary.

UPPER(MANAGED_AR) = 'Bird Islands Sanctuary'

The LIKE operator (instead of the = operator) is used to build a partial string search. For example, the following expression would select both New Brunswick, and Newfoundland and Labrador among CA province names:

NAME Like 'Ne%'

Greater than (>), less than (<), greater than or equal (>=), less than or equal (<=), and BETWEEN operators can be used to select string values based on sorting order. For example, the expression below will select all provinces in a resource that have names starting with the letters R to Z:

NAME >= 'R'

The not equal (<>) operator can also be used in query strings.

back to top

Wildcard Characters

A wildcard character is a symbol that stands for one or more unknown characters.

When searching file-based data, a '%' wildcard is used to indicate that anything is acceptable in its place: one character, multiple characters, or no character. Alternatively, a '_' wildcard is used to represent a single character in a search. For example, the expression below would select any National Park name starting with the letters Au, such as Aulavik and Auyuittuq:

PC_NAME_EN Like 'Au%'

back to top

Null Values

If a column (attribute) of a type that supports null values is selected, and if that column contains any null values in the records displayed in the Values list of the Feature Search dialog, the second entry from the top of the list will be ' '. Double-clicking this value will add it to the expression and, by using the = operator, the query on the column will select all records with a null value for the attribute. For example, Element Occurrence records with a null value for ELCODE would be returned with the following expression.

ELCODE = ' '

To select all records for which an attribute is not null, the <> (not equal) operator is used. The query shown below would return all occurrences that have ELCODE values, that is, where the ELCODE attribute is not null.

ELCODE <> ' '

back to top

Querying numbers

Numbers can be included in a query using the equal (=), not equal (<>), greater than (>), less than (<), greater than or equal to (>=), and less than or equal to (<=) operators. The example below would return the provinces having 2001 populations that were greater than 100,000.

POP_2001 > 100000

A point is always used as the decimal delimiter regardless of regional settings. However, the comma cannot be used as a decimal or thousands delimiter in a query.

back to top

Calculations

Calculations can be included in queries using the arithmetic operators for addition (+), subtraction (-), multiplication (*), and division (/).

Calculations can be performed between fields and numbers. In the example below, any feature having an area greater than or equal to its length multiplied by 100 would be returned by the query.

SHAPE_AREA >= SHAPE_LEN * 100

Calculations can also be performed between fields. For example, to find the provinces with a population density of less than or equal to 25 people per square kilometer, the following expression could be used:

POP_2001 / AREA_KM <= 25

back to top

Operator precedence

Expressions are evaluated according to standard operator precedence rules. For example, the part of an expression enclosed in parentheses is evaluated before the part that is not enclosed.

This example:

HOUSEHOLDS > MALES * POP90_SQMI + AREA

is evaluated differently, and thus produces different results, than:

HOUSEHOLDS > MALES * (POP90_SQMI + AREA)

To use parentheses in a query expression, either click to add the parentheses and then enter the expression to be enclosed, or highlight the existing expression to be enclosed and then press the Parentheses button to enclose it.

back to top

Combining expressions

Expressions can be combined together with the AND and OR operators. When the AND operator is used, both of the expressions separated by the AND operator must be true for a record to be selected.

AREA_KM > 100000 AND DWELL_2001 < 50000

When the OR operator is used, at least one of the two expressions separated by the OR operator must be true for a record to be selected.

AREA_KM > 100000 OR POP_2001 > 750000

Use the NOT operator at the beginning of an expression to find features or records that do not match the specified expression. NOT expressions can be combined with AND and OR.

AREA_KM > 100000 AND NOT POP_2001 < 750000

back to top

Querying dates

The syntax required for querying dates depends on the data type. True DATE fields will be stored in the format: 'yyyy-mm-dd hh:mm:ss'. Specify the format within your query as shown below.

Given the format, even a single date requires querying for a range, due to the inclusion of time. Utilize the following query to return data mapped on July 1, 2013:

DIGITAL_MAPPING_DATE >= DATE '2013-07-01 00:00:00' AND DIGITAL_MAPPING_DATE <= DATE '2013-07-01 23:59:59'

Similarly, to find data mapped anytime in July 2013:

DIGITAL_MAPPING_DATE >= DATE '2013-07-01 00:00:00' AND DIGITAL_MAPPING_DATE <= DATE '2013-07-31 23:59:59'

back to top

Related Topics:

Feature Search

- Filter

Make A Map

The Make a Map tab within the map enables the addition of annotation (graphics and text) to the map. These annotations can be used to Create Project. The contents of the tab are segregated into accordion sections which can be contracted by clicking the  button or expanded by clicking the  button.

Polygons

- Lines

- Points

- Text

- Annotation Layer Settings

Polygons

Zoom to the area of interest.

- From the Drawing Type dropdown, select Polygons.

- Click Add  to start drawing. The Draw/Edit toolbar and Annotation Settings section will appear.

- Within the Annotation Settings section, select the desired Fill Style, Fill Color, Transparency, Outline Style, Outline Color and Outline Thickness.

- Draw a polygon(s) or use the Additional Mapping Options tool to copy a polygon(s) from an existing Map resource.

- Within the Draw/Edit toolbar, click Accept.

- To change the annotation, click the Edit Annotations  button within the Annotation Layer Settings section and click the annotation to edit.

back to top

Lines

Zoom to the area of interest.

- From the Drawing Type dropdown, select Lines.

- Click Add  to start drawing. The Draw/Edit toolbar and Annotation Settings section will appear.

- Within the Annotation Settings section, select the desired Line Style, Line Color, Transparency, and Line Thickness.

- Draw a line(s) or use the Additional Mapping Options tool to copy a line(s) from an existing Map resource.

- Within the Draw/Edit toolbar, click Accept.

- To change the annotation, click the Edit Annotations  button within the Annotation Layer Settings section and click the annotation to edit.

back to top

Points

Zoom to the area of interest.

- From the Drawing Type dropdown, select Points.

- Click Add  to start drawing. The Draw/Edit toolbar and Annotation Settings section will appear.

- Within the Annotation Settings section, select the desired Fill Style, Symbol Size, Fill Color, Transparency, Outline Color and Outline Thickness.

- Click the map to place the point(s) on the map or use the Additional Mapping Options tool to copy a point(s) from an existing Map resource.

- Within the Draw/Edit toolbar, click Accept.

- To change the annotation, click the Edit Annotations  button within the Annotation Layer Settings section and click the annotation to edit.

back to top

Text

Zoom to the area of interest.

- From the Drawing Type dropdown, select Text.

- Within the Annotation Settings section, enter the Text to Add within the text box and then select the desired Text Color, Text Size, Text Align, Text Angle, Text Style, and Text Weight.

- Click Add  and then click on the map where you would like the text placed.

- Repeat steps 3 & 4 to add the same text in multiple locations or enter different text.

- To change the annotation, click the Edit Annotations  button within the Annotation Layer Settings section and click the annotation to edit.

back to top

Annotation Layer Settings

The configurations within the Annotation Layer Settings section apply to all annotations added to the map.

Visibility - set to display annotation by default. Uncheck the Visibility checkbox to turn off all annotation.

- Transparency – allows the transparency of the layer to be adjusted by sliding the indicator along the bar.

- Clear All Annotations -  removes all annotations from the map.

- Edit Annotations -  allows for editing of individual annotations:

- Click the Edit Annotations button

- Select the desired annotation to edit - the accordion section for the annotation type will be expanded to provide access to the appropriate settings.

- Point - change the settings of the Point or change its location by clicking on it and dragging the point to the desired location.

- Line - change the settings of the Line or change its location by clicking on it and editing the spatial feature.

- Polygon - change the settings of the Line or change its location by clicking on it and editing the spatial feature.

- Edit spatial feature by:

- Dragging, rotating, expanding, or shrinking the entire feature; and/or by

- Adding, deleting, or dragging vertices.

- Text - change the Alignment or Color of the Text or change its location/angle by clicking and dragging the text to the desired location.

- Click Stop Editing  after making the desired changes or the Delete Annotation button to delete the feature.

back to top

Related Topics:

Draw/Edit Toolbar

- Additional Mapping Options

- Print

Draw/Edit

The Draw/Edit toolbar opens automatically upon choosing to Create a Project or add a spatial feature via Make a Map.

If accessed via Create a Project and the map is not zoomed in closer than 1:72,224, only the Upload Shapes tool will be available. To access the other draw tools, zoom in to 1:72,224 or closer using the Scale Bar or Zoom to Coordinates or Scale tool.

A number of different tools are provided on the Draw/Edit toolbar, enabling various actions ranging from digitizing a shape, to moving boundaries, to removing an area from within feature, to buffering a polygon. Some of these tasks require different modes, which are displayed on the lower left of the toolbar.

Draw Shape

- Edit Shape:

- Edit Geometries

- Erase Inside Drawn Area

- Crop Outside Drawn Area

- Upload Shapes

- Buffer Shape

- Additional Mapping Options:

- Map Layers

- Make a Map

- Coordinates

- Drawing a point or line feature(s)

- Other Draw/Edit Tools:

- Undo

- Redo

- Clear Shape

- Draw Settings

- Use Freehand

- Disable Navigation while Drawing

Draw Shape

The default tool within the Draw/Edit toolbar, Draw Shape, is limited to drawing polygonal features. To digitize a point or line feature(s), utilize the Drawing option within the Additional Mapping Options tool.

Features can be digitized using either the default drawing tool, which utilizes vertices, or a freehand tool.

Use default Draw Shape tool:

If not already in Draw mode, click the  Draw Shape icon.

- Single click to draw a point.

- For lines and polygons, click every location a vertex is to be placed and double-click to complete feature.

back to top

Use Freehand drawing tool:

- From the Draw Settings dropdown, select Use Freehand.

- Holding down the mouse button, draw the feature.

- Release the mouse button to finish digitizing the feature.

- Click Accept to complete the feature.

- Alternatively, use the edit tools described in the following sections to make changes to the feature before clicking Accept to save.

back to top

Edit Shape

Edit Entire Shape and/or Vertices

Enter Edit mode by clicking the  Edit Shape icon.

- The vertices and extent of the feature will be displayed.

- Edit feature by:

- Dragging, rotating, expanding, or shrinking the entire feature; and/or by

- Adding, deleting, or dragging vertices.

back to top

Erase Inside Drawn Area

Enter Erase mode by clicking the  Erase Inside Drawn Area icon.

- Digitize a polygon circumscribing the area to be cut from the feature by single-clicking to add each vertex, and double-clicking to complete the polygon.

- The area circumscribed by the polygon will be clipped from the original feature.

back to top

Crop Outside Drawn Area

Enter Crop mode by clicking the  Crop Outside Drawn Area icon.

- Digitize a polygon that contains the portion of the feature to be retained, by single-clicking to add each vertex, and double-clicking to complete the polygon.

- The area within the polygon drawn in Crop mode will be retained, while that portion of the feature outside the polygon will be deleted.

- Polygon drawn overlapping feature... area of feature within polygon remains after cropping.

back to top

Upload Shapes

Current functionality allows for ESRI shapefiles to be added. To upload a shapefile, all component files must be zipped into a zip file with no additional directories or files. A valid .prj file must be included in the zip file. Maximum file size not to exceed 2 GB.

Enter Upload Shapes mode by clicking the Upload Shapes  icon.

- Within the Upload Shapes dialog, click Select File to Upload .

- Navigate to and select the shapefile to add.

- NOTE: The following message will appear if a projection file (.prj) is not included in the zip file.

- The map will zoom to the extent of the spatial feature(s) within the uploaded file.

- If a file with multiple shapes has been selected, draw a box on the map to select the desired feature(s) within the uploaded layer.

- The Details dialog of the selected feature(s) will be displayed. To remove a feature from the selection, from the Tasks menu, select Remove from Include List. Once removed, the option to Add to Include List becomes available in the Tasks menu.

- The number of features selected will be displayed in the section to the right of the Select From Resource button along with a View button, which allows the user access to the Details dialog again if they need to remove additional features from the selection. Alternatively, create a new selection by clicking the Select from Resource button again (return to Step 4a for instructions).

- Click Accept within the Upload Shapes dialog.

- In the Draw/Edit toolbar click Accept.

back to top

Buffer Shape

The Buffer Shape tool can be used in conjunction with the Draw Shape tool or Additional Mapping Options.

Either draw a shape using the Draw Shape tool or create a shape using the Additional Mapping Options tool.

- Enter Buffer mode by clicking the  Buffer Shape icon.

- In the Buffer dialog, enter a buffer Distance and select the desired distance unit from the dropdown. Click Buffer.

- Use of Buffers

- A positive distance will buffer outside the feature whereas a negative distance will buffer within the feature. Negative distances cannot exceed the size of the shape, nor can they be used with Point or Line features. The following error will be displayed when the negative distance exceeds the size of the shape.

- Buffers are additive. Thus, if one distance is used to buffer a polygon and then another distance is entered, the second buffer will be added to the first buffer rather than to the original feature. For example, if a feature is first buffered by 5000 m, and then a second buffer distance of 2500 m is specified, the original feature ends up being buffered by 7500 m; the second distance does not replace the first.

- To apply different buffers to a polygon without combining them,  Undo Last Drawing Change must be used before specifying the second buffer distance. This will cause the original buffer to be removed prior to applying the second.

- The buffer will be applied and the user is returned to the Draw/Edit toolbar to further modify the feature, if desired. Click Next to continue the process.

back to top

Additional Mapping Options

The Additional Mapping Options dialog allows the user to:

copy a shape from Map Layers

- copy shapes created via Make a Map

- enter Coordinates

- create a Drawing

- This tool can be used reiteratively for multiple edits and use of various tools within a given editing session. As such, the Additional Mapping Options To: is used to indicate how to use the new shape:

- Add to original drawing

- Replace original drawing

- Erase areas of overlap

- Crop to copied feature

- Following are the instances when this dialog will be displayed:

- If there is a drawing in the primary draw toolbar whose feature type (point, line, polygon) is the same as the current shape, then the Add to original drawing and Replace original drawing options will be available.

- If there is a drawing in the primary draw toolbar and the feature type of the current shape is a polygon, then the Erase areas of overlap and Crop to copied feature options will be available.

- If the feature type of the drawing in the primary draw toolbar is polygon, as is that of the current shape, then all 4 options will be available.

back to top

Map Layers

Click the  Additional Mapping Options  icon.

- In the Additional Mapping Options dialog, from the Source dropdown menu, select Map Layers.

- From the Resource dropdown menu, select the map resource from which to copy the shape(s). The options depend on the layers available within the Layers section of the map.

- NOTE: If the chosen Resource is comprised of multiple layers, an additional Layer dropdown list will be displayed from which to select the given layer to copy the shape(s).

- Click the Select from Resource button and holding the mouse button down, draw a box on the map to select the desired feature(s) within the Resource/Layer.

- The Details dialog of the selected feature(s) will be displayed. To remove a feature from the selection, from the Tasks menu, select Remove from Include List. Once removed, the option to Add to Include List becomes available in the Tasks menu.

- The number of features selected will be displayed to the right of the Select From Resource button along with a View  button, which allows the user access to the Details dialog again if they need to remove additional features from the selection. Alternatively, create a new selection by clicking the Select from Resource button again (return to Step 4 for instructions).

- To further modify the selected features, click Modify or Next to use the features as they exist.

- In the Draw/Edit toolbar click Accept unless further edits are needed.

back to top

Make a Map

Click the  Additional Mapping Options  icon.

- In the Additional Mapping Options dialog, from the Source dropdown menu, select Make a Map.

- Click the Select from Resource button and click on the desired feature(s).

- The number of features selected will be displayed in the Spatial Search section to the right of the Select From Resource button along with a View button, which allows the user access to the Details dialog again if they need to remove additional features from the selection. Alternatively, create a new selection by clicking the Select from Resource button again (return to Step 2 for instructions).

- To further modify the selected features, click Modify or Next to use the features as they exist.

- In the Draw/Edit toolbar click Accept unless further edits are needed.

back to top

Coordinates

Click the  Additional Mapping Options  icon.

- In the Additional Mapping Options dialog, from the Source dropdown menu, select Coordinates.

- Select the desired Projection and enter in the formats shown:

- Latitude/Longitude (DMS)

- Latitude (Northing): 42d 42' 44"

- Longitude (Easting): -75d 38' 38"

- Latitude/Longitude (Decimal)

- Latitude (Northing): 42.712326430204115

- Longitude (Easting): -75.64402639639827

- Subnational Projection - the projection used by your HP/CDC within the Biotics application. Contact your Biotics Administrator for further information.

- Define Projection

- NOTE: WKID and WKT values can be found here.

- By Well Known ID (WKID): 3857

- Latitude (Northing): 5268287

- Longitude (Easting): -8420654.5

- By Well Known Text (WKT):

- The WKT can be copied directly from a projection file (.prj). Below is an example.

- PROJCS["WGS_1984_Web_Mercator_Auxiliary_Sphere",GEOGCS["GCS_WGS_1984",DATUM["D_WGS_1984",SPHEROID["WGS_1984",6378137.0,298.257223563]],PRIMEM["Greenwich",0.0],UNIT["Degree",0.0174532925199433]],PROJECTION["Mercator_Auxiliary_Sphere"],PARAMETER["False_Easting",0.0],PARAMETER["False_Northing",0.0],PARAMETER["Central_Meridian",0.0],PARAMETER["Standard_Parallel_1",0.0],PARAMETER["Auxiliary_Sphere_Type",0.0],UNIT["Meter",1.0],AUTHORITY["ESRI","102100"]]

- Latitude (Northing): 5268287

- Longitude (Easting): -8420654.5

- Click Zoom and Preview.

- To further modify the selected features click, Modify or Next to use the features as they exist.

- In the Draw/Edit toolbar click Next unless further edits are needed.

back to top

Drawing

This option enables drawing of any feature type (Point, Line, Polygon) whereas the default Draw Shape tool within the Draw/Edit toolbar is limited to polygonal features.

Click the Additional Mapping Options  icon.

- In the Additional Mapping Options dialog, from the Source dropdown menu, select Drawing.

- From the Type dropdown menu, select the type of spatial feature (Point, Line, or Polygon) to draw and click Next.

- The Draw shape to use as other Source dialog will be displayed. Draw the desired shape and click Next.

- Single click to draw a point.

  - For lines and polygons, click every location a vertex is to be placed (unless the Use Freehand option is selected) and double-click to complete feature.

In the case of a line or polygon feature, the Draw/Edit toolbar will be displayed, allowing the user to edit the feature further. Click Next to continue.

back to top

Other Draw/Edit Tools

Undo

- Redo

- Clear Shape

- Draw Settings The Draw Settings dropdown menu includes two options:

- Use Freehand provides the ability to digitize a feature freehand rather than by clicking to add individual vertices.

- Disable Navigation while Drawing - a setting that is on by default - improves drawing performance by switching map navigation (i.e., pan and zoom functionality) off once the first vertex of a shape has been placed, and re-enabling navigation when the shape is closed. Leaving this draw setting enabled prevents the application from interpreting a longer touch on the cursor while digitizing as an attempt to pan, which would cause the map to be refreshed and any vertices digitized to be lost.

back to top

Related Topics:

Create a Project

- Make a Map

- Projected Coordinate System Tables (WKID lookup)

- Scale Bar

- Zoom to Coordinates or Scale

Map Navigation

Several categories of tools are available for efficiently moving to specific locations and changing the display in the map viewer.

Navigation Tools:

- Find Address or Place

- Scale bar

- Zoom to Coordinates or Scale

- Overview map

- Spatial Bookmarks

- Extent tools:

- Default Extent

- Previous Extent

- Next Extent tools

- Shortcuts:

- Zoom In

- Zoom Out

Scale Bar

Slide the scale bar up and down to zoom in and out respectively, changing the map extent.

NOTE: the map scale and coordinates are visible in the bottom left hand corner of the map viewer (example below) and change accordingly when the scale bar or any other navigation tools are used.

back to top

Extent tools

Default Extent

To zoom to the initial extent of the map, click the  Default Extent  icon located in the upper right corner of the map title bar.

Previous Extent

To zoom to the previous extent of the map, click the  Previous Extent  icon located in the upper right corner of the map title bar.

Next Extent

To zoom to the next extent of the map, click the Next Extent  icon located in the upper right corner of the map title bar.

back to top

Shortcut Tricks

Zoom in - Hold the SHIFT key while dragging a box on the map.

Zoom out - Hold SHIFT and CTRL keys while dragging a box on the map.

back to top

Related Topics:

Find Address or Place

- Overview Map

- Zoom to Coordinates or Scale

Find Address or Place

This tool navigates to locations on the map using the ArcGIS Geocoder as the source of the data.

Steps:

Found in the upper right corner of the Map, the Find address or place tool uses the ArcGIS Geocoder as the source of the search, by default.

- Enter the desired location (i.e., Strawberry, AZ) in the Find address or place text box .

- Click <Enter> or click the Find  icon to zoom to the specified location on the map.

- NOTE: An alternate mode of zooming to a specific location, in cases when the desired location is not found, is to use the Feature Search tool to find the location within one of the map layers, and then zoom to it.

back to top

Related Topics:

Feature Search

- Map Navigation

Overview Map

The Overview Map, located in the upper right corner of the map, is useful for keeping track of your location within the state when zoomed into an area on the main map.

Show the Overview Map by clicking the arrow  icon.

- Hide the Overview Map by clicking the arrow  icon in the upper right corner.

- Change the map extent by dragging the gray box within the Overview Map. The main map adjusts when the mouse button is released.

back to top

Related Topics:

Map Navigation

Spatial Bookmarks

Bookmark the map at a particular extent and location to return to for later use during the same logged in session.

Steps:

Within the Map menu, navigate to the desired location.

- Click the Spatial Bookmarks  icon located in the upper right corner of the map title bar.

- Within the Spatial Bookmark dialog:

- Add a bookmark by clicking Add Bookmark to enter a name for the bookmark. Hit the TAB or ENTER key on the keyboard to save the bookmark.

- Edit a bookmark name by clicking the Edit icon  and editing the name of the bookmark. Hit the TAB or ENTER key on the keyboard to save the bookmark.

- Remove a bookmark by clicking the Remove icon

- Zoom to an existing spatial bookmark by clicking its name.

back to top

Related Topics:

Map Navigation

Zoom to Coordinates or Scale

This navigation tool is used to quickly adjust the map display according to either the coordinates or map scale specified by the user.

Steps:

Within the Map, click the Zoom To Coordinates or Scale  icon located in the upper right corner of the map title bar.

- The Zoom To Coordinates or Scale dialog opens, displaying the current map scale and coordinates, as indicated on the map by a red diamond.

- Select the desired Scale.

- To zoom to a different location, select the Projection and enter the desired Latitude (Northing) and Longitude (Easting). Alternatively, with the Click for the Map for Coordinates  checkbox indicated, click anywhere on the map to view the coordinates of that location, in the selected Projection. Coordinates can be entered in the following projections in the formats shown:

- Latitude/Longitude (DMS)

- Latitude (Northing): 42d 42' 44"

- Longitude (Easting): -75d 38' 38"

- Latitude/Longitude (Decimal)

- Latitude (Northing): 42.712326430204115

- Longitude (Easting): -75.64402639639827

- UTM Zone 17 or UTM Zone 18

- Latitude (Northing): 4254911.012366921

- Longitude (Easting): -2346228.775082956

- Define Projection

- NOTE: WKID and WKT values can be found here.

- By Well Known ID (WKID):3857

- Latitude (Northing): 5268287

- Longitude (Easting): -8420654.5

- By Well Known Text (WKT):

- The WKT can be copied directly from a projection file (.prj). Below is an example.

- PROJCS["WGS_1984_Web_Mercator_Auxiliary_Sphere",GEOGCS["GCS_WGS_1984",DATUM["D_WGS_1984",SPHEROID["WGS_1984",6378137.0,298.257223563]],PRIMEM["Greenwich",0.0],UNIT["Degree",0.0174532925199433]],PROJECTION["Mercator_Auxiliary_Sphere"],PARAMETER["False_Easting",0.0],PARAMETER["False_Northing",0.0],PARAMETER["Central_Meridian",0.0],PARAMETER["Standard_Parallel_1",0.0],PARAMETER["Auxiliary_Sphere_Type",0.0],UNIT["Meter",1.0],AUTHORITY["ESRI","102100"]]

- Latitude (Northing): 5268287

- Longitude (Easting): -8420654.5

- Click Zoom. A red diamond indicates the location on the map. This is removed when the dialog is closed.

- If only a new map scale is selected, the map viewer will automatically zoom in or out to the selected scale, while remaining in the same location.

- If only coordinates are edited (regardless of a change in projection), the map viewer will zoom to the location defined by the coordinates but remain at the same scale.

- If both map scale and coordinates were changed, the map viewer adjusts location and scale accordingly.

back to top

Related Topics:

Map Navigation

- Projected Coordinate System Tables (WKID lookup)

Measure

The measure tool is used to determine the size of a designated area, the distance of a digitized line, and the coordinates of a specific location.

Steps:

Within the map, click the Measure  icon, located in the upper right corner of the map title bar.

- Select the desired measurement tool and the appropriate unit of measure from the dropdown list.

- Area

- Distance

- Location

- Digitize the feature to be measured:Point - click the desired location

- Line - digitize a line, double-clicking to complete the feature

- Polygon - digitize a polygon, double-clicking to complete the feature

- The Measurement Result is reported in the specified units once the line/polygon has been completed.

- NOTE: The measurement unit can be changed after the feature has been digitized and the measurement result will be displayed in the newly selected unit.

back to top

Related Topics:

Find address or place

- Identify

- Map Navigation

- Zoom to Coordinates or Scale

Print

Allows the user to create a printable version of the map view.

Steps:

Within the Map menu, click the  icon located in the upper right corner of the map title bar.

- Within the Print Map dialog, enter pertinent information within the Title, Author, and Copyright text boxes only if intending to print to Landscape Layout. This information is not utilized by the Map Only print options and hence need not be included if printing the Map Only.

- From the Print dropdown menu , select the desired print option:

- Landscape Layout (PDF) - provides a PDF of the map including the Title, Author, and Copyright information provided.

- Map Only (PDF) - provides a PDF just of the map itself. Neither Title, Author, nor Copyright information is utilized.

- Map Only (PNG) - provides a PNG just of the map itself. Neither Title, Author, nor Copyright information is utilized.

- Map Only (JPG) - provides a JPG just of the map itself. Neither Title, Author, nor Copyright information is utilized.

- The Print dropdown reflects Printing  while the map is being generated.

- The map opens in a separate tab within the web browser. NOTE:The printed map cannot be opened in a new tab unless the pop-up blocker is turned off. If prompted, choose to Always allow pop-ups from this site.

- From the File menu of the web browser, select Save As and indicate where (and with what name the map document should be saved.

back to top

Snapping Settings

Snapping allows you to create features that connect to each other so your edits are more accurate, with fewer errors. When snapping is turned on, your pointer will jump, or snap to, edges, vertices, and other geometric elements when your pointer is near them and within a certain tolerance. This enables you to position a feature easily in relation to the locations of other features.

Snapping is not limited to being used while editing, as it is utilized in other areas such as the Measure tool on the Tools toolbar.

Snapping is useful with many editing operations, such as creating polygons that do not overlap or have gaps between them, drawing lines that connect to each other, or placing a point exactly along an existing line.

Steps:

Within the Map, click the  icon located in the upper right corner of the map title bar, or from the Tools menu, select Snapping Settings.

- Within the Snapping Settings dialog, all feature layers listed within the Layers tab of the Map are available for snapping. Select the layer(s) to which you want to snap from the dropdown menu and click Add . Repeat this step until each of the layers to which should be snapped have been added.

- If the snapping should be limited to vertices only, indicate the Snap Vertices Only checkbox.

- Select the tool with which to snap (i.e. Create Project, Make a Map, Measure).

- Hold CTRL to enable snapping.

- As you move your pointer around the map, the pointer will snap to various geometric locations as you move over them, as indicated by an aqua cross .

- Once the cursor has snapped, click to place a vertex or point or perform the edit as desired. Double-click to complete the spatial feature.

- Within the Snapping Settings dialog, Remove  the layer(s) which is no longer desired for use with snapping.

back to top

Related Topics:

Create Project

- Make a Map

- Measure

Switch Basemap

A basemap provides a background geographical context for the content displayed on a map. Within the map viewer, the basemap can be changed at any time by choosing a layer from the basemap gallery (e.g., topography, imagery, streets) or made invisible.

NOTE: Upon initiating the Conservation Report and Create Project processes, the Switch Basemap tool becomes unavailable. If you wish to change the basemap during these processes, open the Switch Basemap tool prior to initiating the process and leave it open or minimize it until needed.

Steps:

Within the Map, click the Switch Basemap  button, located in the upper left corner of the map title bar.

- Within the Switch Basemap dialog, click the thumbnail of the basemap to be used in the map.

- The basemap in the main map will change accordingly.

- NOTE: The overview map retains the National Geographic basemap in order to ensure that there is always a geographic context, which may not be so evident using the other basemaps.

- To turn off or make the base map invisible, uncheck the toggle box associated with the Basemap layer within the Basemap accordion section of the Layers tab.

back to top

Related Topics:

Add Resources

- Test Map Service

- Map Services

Users

Allows users assigned the Administrator Role the ability to find, view, and sort users of the system. See User Details to assign user Roles and indicate their Status, either Active or Blocked.

Steps:

From the Admin menu, select Users.

- Within the Users page, all Users are listed.

- Filter users

- Sort users

- View users

- Edit users

Filter users

Filter the Users by First name, Last name and/or Organization by selecting a comparison type from the dropdown menu and typing in search text within the corresponding box.

- Click Apply . The projects which meet the filter criteria will be displayed in the table below the filter criteria.

- NOTE: To remove the filter, delete the filter criteria from the text box and click Apply.

back to top

Sort users

Sort users in ascending order by clicking on the desired heading (i.e. Organization).

- Click on the same heading (i.e. Organization), a second time, to sort in descending order.

back to top

View users

Within the table, under the Link heading (column), click view to see additional information pertaining to that User. The User Details page will open, from which you can view the user's data as well as Edit the user.

back to top

Edit users

Within the table, under the Link heading (column), click edit to edit the user's data. additional information pertaining to that User.

The User Details page will open, from which you can:

reset the User's password by updating the Password and Confirm password fields .

- update the User's Status to indicate whether the account is Active or Blocked.

- assign the appropriate Role to the User.

- Click Save once all desired changes have been made.

back to top

Related Topics:

Projects

- User Details

Roles

User Roles are assigned within the Users page. Following are definitions of the different Roles:

authenticated user: merely indicates that they have an account which allows them to log into the application.

- Customer: can create projects and edit their own projects in Draft Status. This is the default privilege assigned to all users.

- Partner: this role has not yet been defined but is being used as a future placeholder.

- Reviewer: can create projects; can view and modify all projects, including those in Final Status.

- MO Admin: has full administrative functionality; can view all projects but cannot create or modify a project.

Related Topics:

Users

- Create Project

- Edit (Project) Details

- Edit/View (Project) Shape

Projects

Allows users assigned the roles of Evaluator/Reviewer or Administrator the ability to find, view, and sort all projects submitted to the system.

Steps:

Depending on your privileges, navigate to the Projects menu (Reviewer) or from the Admin menu, select Projects (Evaluator/Administrator).

- Within the Projects page, all projects are listed.

- Filter projects

- Sort projects

- View project

Filter projects

Projects can be filtered by a number of different attributes.

Select a comparison type from the dropdown menus of one or more of the filter criteria and enter search text within the corresponding box.

- Click Apply . The projects which meet the filter criteria will be displayed in the table below the filter criteria.

- NOTE: To remove the filter, delete the filter criteria from the text box and click Apply.

Sort projects

Sort Projects in ascending order by clicking on the desired heading (i.e. Project ID).

- Click on the same heading (i.e. Project ID), a second time, to sort in descending order.

View project

Within the table, click a Project Title to find additional information pertaining to the Project. The Project Details page will open, from which you can perform additional functionality pertaining to the project.

back to top

Related Topics:

Edit Details

- Edit/View Shape

- Email

- Notes

- Users

Project Details

From within the Project Details page, one can view the details of a project as well as open the associated Report File(s) and Boundary Shapefile(s), upon completion of the project analysis.

Tabs within the Project Details page allow for the following additional functionality:

Edit/View Shape: view the project boundary (Map)

- Generate Report: submit the project for analysis again, without editing either the details or the shape.

- Notes: add a note to the Project, following submission

- Email: email the project Contact with relevant questions.

Steps:

From the Admin menu, select Projects.

- Within the My Projects window, click the project Title to view the project details.

- Within the Project Details page:

- The Project Review Results section reflects the Review Status of the project. Projects which have been edited will include a separate entry within the Project Review Results table, reflecting the results of each project submission.

- Once the Review Status indicates Report Generated (rather than Submitted or Pending), links to the Report File, Boundary Shapefile and Species Results for Export are provided. Click the links to open/save the files.

- The project details are displayed below the Project Review Results section.

- click the Project Type link(s) for a full description of the Project Type(s).

back to top

Related Topics:

Edit/View Shape

- Generate Report

- Notes

- Email

Edit/View Shape

This functionality allows Administrators to view the project's spatial boundary.

Each edition will be reflected within the Project Details page, available via View Project.

Steps:

From the Admin menu, select Projects.

- Within My Projects (or Projects) page, click on the Title of the project to be edited.

- Within the Project Details page, click the Edit/View Shape tab  at the top of the page.

- Within the Map, the project boundary will be displayed.

back to top

Related Topics:

Projects

Generate Report

Submit the project for analysis again, without editing either the details or the shape.

Steps:

Navigate to the My Projects menu. NOTE: Evaluators and Administrators access Projects via the Admin menu.

- Within My Projects (or Projects) page, click on the Title of the project to be edited.

- Within the Project Details page, click the Generate Report tab  at the top of the page.

- Within the Generate Report page, click Submit to generate a new project report.

back to top

Related Topics:

Create Project

- Edit/View Shape

- My Projects

- View Project

Notes

Allows the user to add a note to the Project, following submission.

Steps:

Access the Projects page by navigating to the Projects menu (Reviewer) or the Projects option within the Admin menu (Evaluator/Administrator).

- Within the Projects page, click on the Title of the project to be edited.

- Within the Project Details page, click the Notes tab  at the top of the page.

- Within the Notes page, click the Add a note link  below the Project Review Results section.

- Enter the desired note within the expanded Add a note section and click Save Note.

back to top

Related Topics:

Create Project

- Edit Details

- Edit/View Shape

- Projects

Email

Evaluators and Administrators of the system have additional privileges which enable them to email the project Contact with relevant questions.

Steps:

Access the Projects page by navigating to the Projects menu (Reviewer) or the Projects option within the Admin menu (Evaluator/Administrator).

- Within the Projects page, all projects are listed. Click the Project Title of the desired project.

- Within the Project Details page, click the Email tab  to send an email to the Contact person for the project.

- The email form will be autopopulated with the email address of the contact (To) as well as the title of the project in the Subject line. Within the body of the email, replace (insert message here) with the pertinent message.

- Click Send  to send the email.

back to top

Related Topics:

Projects

Project Types

This functionality allows users assigned the Administrator Role the ability to configure the list of Project Types available when submitting a Project. After creating a new Project Type, it needs to be associated with a Project Type Recommendation. Either edit an existing Project Type Recommendation or create a new one.

Search

- Add

- Re-order

- Disable

- Activate Watershed Search

- Go to the term page

Search

From the Admin menu, select Project Types.

- Within the Project Types page, click the Search  button within the Toolbar. Search methods include:

- Search all Project Types

- Search specific Project Types

Search all Project Types

Enter a Search String to search throughout all Project Types. Results matching the Search String are automatically displayed.

- Select the desired Project Type from the dropdown list and click the Search  button within the Search section.

back to top

Search Specific Project Types

To search within specific Project Types, enter a Search String and indicate the Project Types in which to search within the Project Type tree.

- Mark the checkbox to Search under selected terms and click the Search  button within the Search section.

- The results will be displayed within a new page. Within the Project Type section, select the Project Type of interest. 
NOTE: Click Show unfiltered tree within the header message to return to the full Project Types page.

- The selected Project Type is displayed within the Project Type tree along with its details.

- The details of the Project Type are editable, including Name, Buffer Value, and Buffer Unit. The Project Type can also be Disabled such that it will no longer be a Project Type option when a User submits a Project.

- If edits are made, Save Changes .

- A message will be displayed indicating that the term data has been updated.

back to top

Add Project Type

From the Admin menu, select Project Types.

- Within the Project Types page, navigate to the section within the Project Type tree to add the new Project Type. Mark the level under which the Project Type should be added.

- Click Add  within the Toolbar section.

- Within the Add new terms section, enter the name of the new Project Type under Terms. Click Add.

- A message will be displayed indicating that the term has been added.

- By default, the Buffer Value (distance) for the Project Type is set to 1 Mile. To edit this, select the Project Type within the tree to display its details.

- The details of the Project Type are editable, including Name, Buffer Value, and Buffer Unit. The Project Type can also be Disabled such that it will no longer be a Project Type option when a User submits a Project.

- If edits are made, Save Changes .

- A message will be displayed indicating that the term data has been updated.

back to top

Re-order Project Types

From the Admin menu, select Project Types.

- Within the Project Types page, search for the desired Project type or navigate to the section within the Project Type tree.

- There are two ways to re-order the entries within the Project Type tree:

- Mark the checkbox of the term within the tree to re-order and click the Up  and Down  buttons within the Toolbar section, as appropriate.

- Hover over the desired Project Type within the tree to access the controls to re-order the term within the tree (move up  or move down ).

back to top

Disable Project Type

From the Admin menu, select Project Types.

- Within the Project Types page, search for the desired Project type or navigate to the section within the Project Type tree.

- Click the desired Project Type to display its details.

- Within the details section, indicate that it should be Disabled.

- Save Changes .

- A message will be displayed indicating that the term data has been updated.

back to top

Activate Watershed search

Activate the Watershed search to include , in the project report, a list of all EOs in the watershed(s) (Digit-12) which is intersected by the buffered project boundary.

From the Admin menu, select Project Types.

- Within the Project Types page, search for the desired Project type or navigate to the section within the Project Type tree.

- Click the desired Project Type to display its details.

- Within the details section, indicate Watershed Search.

- Save Changes.

- A message will be displayed indicating that the term data has been updated.

back to top

Go to Term Page

From the Admin menu, select Project Types.

- Within the Project Types page, search for the desired Project type or navigate to the section within the Project Type tree.

- Hover over the desired Project Type within the tree to access the controls and click the Go to term page  icon.

- Alternatively, click the desired Project Type to display its details.

- Within the details, click Go to the term page.

back to top

Related Topics:

Project Type Recommendations

Dynamic Analysis

This functionality allows users assigned the Administrator Role the ability to find, sort, view, and create Dynamic Analysis report text within the system.

Dynamic Analysis report text are displayed within the project report only when a feature within the layer is identified during the project analysis. Dynamic Analysis Report Text is linked to a specific layer used in the project analysis. In contrast, Static Structure report text is always displayed in the report, regardless of the results of the analysis. The Project Type report text included in the project report corresponds to that identified by the client when creating the project.

View

- Create

- Edit

- Delete

Steps:

From the Admin menu, within the Report Texts section, select Dynamic Analysis.

- Within the Dynamic Analysis Report Text page, all Dynamic Analysis report texts are listed.

- Filter the report texts by Title or Report Text Language by selecting a comparison type from the dropdown menu and typing in search text within the corresponding box. Click Apply . NOTE: To remove the filter, delete the filter criteria from the text box and click Apply.

- Sort Dynamic Analysis report text in ascending order by clicking on the desired heading (i.e. Title).

- Click on the same heading (i.e. Title), a second time, to sort in descending order.

back to top

View

Within the Dynamic Analysis Report Text page, click the Title of the text to view.

back to top

Create

Within the Dynamic Analysis Report Text page, click Create Report Text  to create new text for inclusion in the project report.

- Within the Create Report Text page, enter:

- Title: create a meaningful title for yourself. This title will not be displayed within the report

- Type: from the dropdown menu, select the type of report text this applies to - in this case Dynamic Analysis:

- Dynamic Analysis: only displayed within the project report when a feature within the given layer detects a conflict during the project analysis. Dynamic Analysis Report Text is linked to a specific layer used in the project analysis.

- Static Structure: always displayed in the report, regardless of the results of the analysis.

- Project Type: text displayed within the project report is dependent on the Project Type defined within the Project.

- Project Type: this only applies when Project Type is selected from the Type dropdown. Indicate all Project Types to which the text should apply.

- Body: indicate the text to display in the project report

- Click Save  at the bottom of the page to save the changes.

- At the top of the page, a message is displayed indicating that the text has been created successfully.

back to top

Edit

Within the Dynamic Analysis Report Text page, click the Title of the text to view.

- Within the Dynamic Analysis Report Text Details page, click the Edit  menu.

- Make the desired edits and click Save  at the bottom o f the page to save the changes.

- At the top of the page, a message is displayed indicating that the Report Text has been successfully updated.

back to top

Delete

Within the Dynamic Analysis Report Text page, click the Title of the text to view.

- Within the Dynamic Analysis Report Text Details page, click the Edit  menu.

- Within the Edit Report Text page, click the Delete button  at the bottom o f the page to delete the Layer.

- A prompt appears confirming that the layer should be deleted. Click Delete to confirm or Cancel to cancel the deletion.

- At the top of the page, a message is displayed indicating that the Layer has been successfully deleted.

back to top

Related Topics:

Analysis Layer

- Analysis Layer Attributes

- Analysis Layer Triggers

- Project Type

- Static Structure

Static Structure

This functionality allows users assigned the Administrator Role the ability to find, sort, view, and create Static Structure report text within the system. After creating the Static Structure, submit a ticket to the ERT Help Desk indicating the Title of the Static Structure report text and where it should be included in the project report.

Static Structure report text is always displayed in the report, regardless of the results of the analysis. In contrast, Dynamic Analysis report text are displayed within the project report only when a feature within the layer is identified during the project analysis. Dynamic Analysis Report Text is linked to a specific layer used in the project analysis. The Project Type report text included in the project report corresponds to that identified by the client when creating the project.

View

- Create

- Edit

- Delete

Steps:

From the Admin menu, within the Report Texts section, select Static Structure.

- Within the Static Structure Report Texts page, all Static Structure report texts are listed.

- Filter the report texts by Title or Report Text Language by selecting a comparison type from the dropdown menu and typing in search text within the corresponding box. Click Apply . NOTE: To remove the filter, delete the filter criteria from the text box and click Apply.

- Sort Static Structure report text in ascending order by clicking on the desired heading (i.e. Title).

- Click on the same heading (i.e. Title), a second time, to sort in descending order.

back to top

View

Within the Static Structure Report Texts page, click the Title of the text to view.

back to top

Create

Within the Static Structure Report Texts page, click Create Report Text  to create new text for inclusion in the project report.

- Within the Create Report Text page, enter:

- Title: create a meaningful title for yourself. This title will not be displayed within the report

- Type: from the dropdown menu, select the type of report text this applies to:

- Dynamic Analysis: only displayed within the project report when a feature within the given layer detects a conflict during the project analysis. Dynamic Analysis Report Text is linked to a specific layer used in the project analysis.

- Static Structure: always displayed in the report, regardless of the results of the analysis.

- Project Type: text displayed within the project report is dependent on the Project Type defined within the Project.

- Project Type: this only applies when Project Type is selected from the Type dropdown. Indicate all Project Types to which the text should apply.

- Body: indicate the text to display in the project report

- Click Save  at the bottom of the page to save the changes.

- At the top of the page, a message is displayed indicating that the text has been created successfully.

- Submit a ticket to the ERT Help Desk indicating the Title of the Static Structure report text and where it should be included in the project report.

back to top

Edit

Within the Static Structure Report Texts page, click the Title of the text to view.

- Within the Static Structure Report Text Details page, click the Edit  menu.

- Make the desired edits and click Save  at the bottom o f the page to save the changes.

- At the top of the page, a message is displayed indicating that the Report Text has been successfully updated.

back to top

Delete

Within the Static Structure Report Texts page, click the Title of the text to view.

  - Within the Static Structure Report Text Details page, click the Edit  menu.

- Within the Edit Report Text page, click the Delete button  at the bottom o f the page to delete the Layer.

- A prompt appears confirming that the layer should be deleted. Click Delete to confirm or Cancel to cancel the deletion.

- At the top of the page, a message is displayed indicating that the Layer has been successfully deleted.

back to top

Related Topics:

Dynamic Analysis

- Project Type

Analysis Layers

This functionality allows users assigned the Administrator Role the ability to find, sort, view, and create Analysis Layers within the system. Analysis Layers are used within the spatial analysis to detect conflicts between a project boundary and the analysis layer. Unlike Layers, Analysis Layers are not displayed within the Map.

View

- Create

- Edit

- Delete

Steps:

From the Admin menu, within the Analysis Layer Rules section, select Analysis Layers.

- Within the Analysis Layers page, all Analysis Layers are listed.

- Filter the Analysis Layers by Title by selecting a comparison type from the dropdown menu and typing in search text within the corresponding box. Click Apply . NOTE: To remove the filter, delete the filter criteria from the text box and click Apply.

- Sort Layers in ascending order by clicking on the desired heading (i.e. Report Text).

- Click on the same heading (i.e. Report Text), a second time, to sort in descending order.

back to top

View

Within the Analysis Layers page, click the Title to view the Analysis Layer Details.

back to top

Create

Within the Analysis Layers page, click Create Analysis Layer to create a new Analysis Layer for inclusion in the analysis.

- Within the Create Analysis Layer page, enter:

- Title

- Analysis Layer Name: the name of the Analysis Layer;

- Report Text Link: select the Dynamic Analysis report text to be included in the report when a conflict is detected with this analysis layer.

- Click Save  at the bottom of the page to save the changes.

- At the top of the page, a message is displayed indicating that the Layer has been created successfully.

back to top

Edit

Within the Analysis Layers page, click the Title of the layer to edit.

- Within the Analysis Layer Details page, click the Edit  menu.

- Make the desired edits and click Save at the bottom o f the page to save the changes.

- At the top of the page, a message is displayed indicating that the Layer has been successfully updated.

back to top

Delete

Within the Analysis Layers page, click the Title of the appropriate analysis layer.

- Within the Analysis Layer Details page, click the Edit  menu.

- Within the Edit Analysis Layer page, click the Delete button  at the bottom of the page to delete the Layer.

- A prompt appears confirming that the layer should be deleted. Click Delete to confirm or Cancel to cancel the deletion.

- At the top of the page, a message is displayed indicating that the Layer has been successfully deleted.

back to top

Related Topics:

Analysis Layer Attribute

- Dynamic Analysis

- Layer Group

- Layers

Analysis Layer Attribute

This functionality allows users assigned the Administrator Role the ability to find, sort, view, and create Analysis Layer Attributes within the system. One or more Analysis Layer Attribute is defined for each Analysis Layer. The Analysis Layer Attribute value(s) is reported when the spatial analysis detects conflicts between a project boundary and the Analysis Layer.

NOTE: The Analysis Layer has to currently exist in the system. If not, then prior to creating an Analysis Layer Attribute, Create Analysis Layer.

View

- Create

- Edit

- Delete

View

From the Admin menu, within the Analysis Layer Rules section, select Analysis Layer Attributes.

- Within the Analysis Layer Attributes page, all configured Analysis Layer Attributes are listed.

- Filter the Analysis Layer Attributes by Title or Intersection Attribute by selecting a comparison type from the dropdown menu and typing in search text within the corresponding box. Click Apply . 
NOTE: To remove the filter, delete the filter criteria from the text box and click Apply.

- Click the Title to view the Analysis Layer Attribute Details.

back to top

Create

From the Admin menu, within the Analysis Layer Rules section, select Analysis Layer Attributes.

- Within the Analysis Layer Attributes page, click Create Analysis Layer Attribute  to create a new Analysis Layer Attribute for inclusion in the analysis.

- Within the Create Analysis Layer Attribute page, enter:

- Title

- Analysis Layer Link: from the dropdown menu, select the Analysis Layer with which the attribute is associated; NOTE: If the attribute is associated with a new Analysis layer, Create Analysis Layer first.

- Intersection Attribute: enter the exact layer attribute name (case sensitive!) to be used in the analysis, as defined within the layer's table. The attribute value will be included in the report when a conflict is detected with this analysis layer. NOTE: Within the map service details, the various attributes associated with a layer can be found within the Fields section of the layer page.

- Click Save  at the bottom of the page to save the changes.

- At the top of the page, a message is displayed indicating that the Layer has been created successfully.

back to top

Edit

From the Admin menu, within the Analysis Layer Rules section, select Analysis Layer Attributes.

- Within the Analysis Layer Attributes page, click the Title of the layer to edit.

- Within the Analysis Layer Attributes Details page, click the Edit  menu.

- Make the desired edits and click Save at the bottom o f the page to save the changes.

- At the top of the page, a message is displayed indicating that the Layer has been successfully updated.

back to top

Delete

From the Admin menu, within the Analysis Layer Rules section, select Analysis Layer Attributes.

- Within the Analysis Layer Attributes page, click the Title of the layer to edit.

- Within the Analysis Layer Attributes Details page, click the Edit  menu.

- Within the Edit Analysis Layer Attribute page, click the Delete button at the bottom of the page to delete the Layer.

- A prompt appears confirming that the attribute should be deleted. Click Delete to confirm or Cancel to cancel the deletion.

- At the top of the page, a message is displayed indicating that the Attribute has been successfully deleted.

back to top

Related Topics:

Analysis Layer

- Layer Group

- Layers

Analysis Layer Triggers

This functionality allows users assigned the Administrator Role the ability to find, sort, view, and create Analysis Layer Triggers within the system. One or more Analysis Layer Triggers can be defined for each Analysis Layer Attribute. The Report Text associated with the Analysis Layer Trigger is included in the Project Report when the specified Intersection Attribute Value defined within the Trigger is returned by the spatial analysis upon detecting a conflict between a project boundary and the Analysis Layer for which the Analysis Layer Attribute is defined.

NOTE: Both the Analysis Layer and the Analysis Layer Attribute have to currently exist in the system in order to configure an Analysis Layer Trigger. If not, then prior to creating an Analysis Layer Trigger, Create Analysis Layer and Create Analysis Layer Attribute.

View

- Create

- Edit

- Delete

View

From the Admin menu, within the Analysis Layer Rules section, select Analysis Layer Triggers.

- Within the Analysis Layer Triggers page, all configured Analysis Layer Triggers are listed.

- Filter the Analysis Layer Attributes by Title or Intersection Attribute Value by selecting a comparison type from the dropdown menu and typing in search text within the corresponding box. Click Apply . NOTE: To remove the filter, delete the filter criteria from the text box and click Apply.

- Click the Title to view the Analysis Layer Trigger Details.

back to top

Create

From the Admin menu, within the Analysis Layer Rules section, select Analysis Layer Attributes.

- Within the Analysis Layer Attributes page, click Create Analysis Layer Trigger  to create a new Analysis Layer Trigger for inclusion in the analysis.

- Within the Create Analysis Layer Trigger page, enter:

- Title

- Analysis Layer Attribute Link: from the dropdown menu, select the Analysis Layer Attribute with which the trigger is associated; NOTE: If the attribute is associated with a new Analysis Layer Attribute, Create Analysis Layer Attribute first.

- Intersection Attribute Value: enter the exact layer attribute value (case sensitive!) to be used in the analysis, as defined within the layer's table. When this attribute value is encountered during analysis, the Report

- Report Text Link: from the dropdown menu, select the Dynamic Analysis Report Text to be included in the report when the Intersection Attribute Value is encountered during the analysis. NOTE: If the desired Dynamic Analysis Report Text doesn't yet exist, Create Report Text.

- Click Save  at the bottom of the page to save the changes.

- At the top of the page, a message is displayed indicating that the Layer has been created successfully.

back to top

Edit

From the Admin menu, within the Analysis Layer Rules section, select Analysis Layer Triggers.

- Within the Analysis Layer Triggers page, click the Title of the layer to edit.

- Within the Analysis Layer Triggers Details page, click the Edit  menu.

- Make the desired edits and click Save at the bottom o f the page to save the changes.

- At the top of the page, a message is displayed indicating that the Layer has been successfully updated.

ack to top

Delete

From the Admin menu, within the Analysis Layer Rules section, select Analysis Layer Triggers.

- Within the Analysis Layer Triggers page, click the Title of the layer to edit.

- Within the Analysis Layer Triggers Details page, click the Edit  menu.

- Within the Edit Analysis Layer Trigger page, click the Delete  button at the bottom of the page to delete the Layer.

- A prompt appears confirming that the trigger should be deleted. Click Delete to confirm or Cancel to cancel the deletion.

- At the top of the page, a message is displayed indicating that the Trigger has been successfully deleted.

back to top

Related Topics:

Analysis Layer

- Analysis Layer Attribute

- Layer Group

- Layers

Layer Group

This functionality allows users assigned the Administrator Role the ability to find, sort, view, and create Layer Groups within the system.

As displayed in the screenshot below, Layer Groups are used within the Layers tab of the Map to segregate different layer types.

View

- Create

- Edit

- Delete

Steps:

From the Admin menu, within the Visualization Layers section, select Layer Group.

- Within the Layer Group page, all Layer Groups are listed.

- Filter the Layer Groups by Layer Group Title by selecting a comparison type from the dropdown menu and typing in search text within the corresponding box. Click Apply . NOTE: To remove the filter, delete the filter criteria from the text box and click Apply.

- Sort Layer Groups in ascending order by clicking on the desired heading (i.e. Display Order).

- Click on the same heading (i.e. Display Order), a second time, to sort in descending order.

View

To view the Layer Group Details, click the Layer Group Title .

Create

Within the Layer Group page, click Create Layer Group to create a new Layer Group for inclusion in the Map.

- Within the Create Layer Group page, enter the Layer Group Title, as it should be displayed in the Layers tab.

- Indicate where the Layer Group should be displayed within the Layers tab by indicating the Display Order.

- Click Save  at the bottom of the page to save the changes.

- At the top of the page, a message is displayed indicating that the Layer Group has been created successfully.

back to top

Edit

Within the Layer page, click the Layer Group Title of the layer to edit.

- Within the Layer Details page, click the Edit  menu.

- Make the desired edits and click Save  at the bottom o f the page to save the changes.

- At the top of the page, a message is displayed indicating that the Layer Group has been successfully updated.

back to top

Delete

Within the Layer page, click the Layer Title for the appropriate layer.

- Within the Layer Details page, click the Edit  menu.

- Within the Edit Layer Group page, click the Delete button  at the bottom o f the page to delete the Layer.

- A prompt appears confirming that the layer group should be deleted. Click Delete to confirm or Cancel to cancel the deletion.

- At the top of the page, a message is displayed indicating that the Layer has been successfully deleted.

back to top

Related Topics:

Layer

Layers

This functionality allows users assigned the Administrator Role the ability to find, sort, view, and create Layers for display within the Layers tab of the Map, as shown below. Unlike Analysis Layers, Layers are used only for display, not within the spatial analysis to detect conflicts with a project boundary.

View

- Create

- Edit

- Delete

Steps:

From the Admin menu, within the Visualization Layers section, select Layers.

- Within the Layers page, all Layers are listed.

- Filter the Layers by Layer Title by selecting a comparison type from the dropdown menu and typing in search text within the corresponding box. Click Apply . NOTE: To remove the filter, delete the filter criteria from the text box and click Apply.

- Sort Layers in ascending order by clicking on the desired heading (i.e. Layer Group).

- Click on the same heading (i.e. Layer Group), a second time, to sort in descending order.

back to top

View

Within the Layers page, click the Layer Title to view the Layer Details.

back to top

Create

Within the Layers page, click Create Layer to create a new Layer for inclusion in the Map.

- Within the Create Layer page, enter:

- Layer Title: as it should be displayed in the Layers tab;

- Layer Group: from the dropdown menu, select the Layer Group in which the Layer should be included;

- Display Order: indicate where the Layer should be displayed within the Layer Group;

- URL: of the published map service

- Default Visible: mark the checkbox if the Layer should be visible in the Map by default.

- Use Filter: mark the checkbox if the Filter tool should be enabled for the Layer;

- Find JSON: code which defines the configuration of the Layer for use within the Attribute Search section of the Feature Search tool. By default all visible fields will be available via a text search. Instructions for configuring dropdown menus for use in the Feature Search tool are detailed in the Configure the Feature Search help topic.

- Layer Description: if configured, this information will be displayed within a Layer Description dialog in the map. To view this, within the Map, hover over the layer name and click the dropdown  icon which displays and select View Description.

- Click Save  at the bottom of the page to save the changes.

- At the top of the page, a message is displayed indicating that the Layer has been created successfully.

back to top

Edit

Within the Layers page, click the Layer Title of the layer to edit.

- Within the Layer Details page, click the Edit  menu.

- Make the desired edits and click Save  at the bottom o f the page to save the changes.

- At the top of the page, a message is displayed indicating that the Layer has been successfully updated.

back to top

Delete

Within the Layers page, click the Layer Title for the appropriate layer.

- Within the Layer Details page, click the Edit  menu.

- Within the Edit Layer page, click the Delete button  at the bottom o f the page to delete the Layer.

- A prompt appears confirming that the layer should be deleted. Click Delete to confirm or Cancel to cancel the deletion.

- At the top of the page, a message is displayed indicating that the Layer has been successfully deleted.

back to top

Related Topics:

Configure the Feature Search

- Feature Search

- Layers

- Layer Group

Configure the Feature Search (i.e. Find JSON)

By default, the Attribute Search section of the Feature Search tool utilizes text searches of all visible fields. Given that the data within the layer is not readily exposed, this makes successfully performing an attribute search difficult. The following screenshot shows an example of a layer which contains 3 attributes which are searchable followed by the fourth, Bridge Type, which utilizes a domain list. The Feature Search tool can be configured to limit the fields displayed within the Attribute Search section of the Feature Search tool as well as configure the use of dropdown lists for specified fields.

There are two ways to limit the fields/attributes listed in the Attribute Search section of the Feature Search tool:

Indicate which fields should be visible within the ArcGIS map document (.mxd) prior to publishing (see the Field Aliases & visibility section of the Map Service Specifications for details), or

- Configure the Feature Search tool by writing JSON code to include only those fields for display and enter the code in the Find JSON section of the Layer.

Additionally, there are two ways to define the values within the dropdown list:

Create domain table(s) for the attribute(s) and include the domain table in the ArcGIS map document (.mxd) prior to publishing (see the Domain Tables section of the Map Service Specifications for details), or

- Manually define the values within the JSON code and enter the code in the Find JSON section of the Layer.

Writing the JSON code to configure the Feature Search

Javascript Object Notation (JSON) and can be thought of as groupings of objects with name/value pairs as <name>:<value> in between each matching bracket {}. Arrays of these objects are delimited by square brackets []. It starts with an array of layers in the published map resource, matching the indexes shown within the details of the service (see View Details in Layers help topic).

As can be seen in the example below, all contain a readable name (which should be initialized from the aliases published to the mapservice - see the Field Aliases & visibility section of the Map Service Specifications for details regarding defining aliases), and an attr, which points to the actual attribute being referenced. The attr object is an array of the attributes in the table and how they are treated. By default, that’s all that’s needed and it will assume the attribute is a string match.

Tips for writing successful JSON code

Copy the JSON code from a Layer which already has the Feature Search successfully configured and edit it for use with the new layer - that way you're not creating the code from scratch but utilizing a working example.

- Utilize Notepad++ (freeware downloadable from the internet) or another text editor which helps to identify matching brackets, parenthesis, etc. Dangling or mismatched brackets, parenthesis, etc. will cause the JSON code to fail.

- After saving the JSON code within the Layer, immediately test the Attribute Search section of the Feature Search tool for the configured layer to verify that it is working successfully. If the Map is already open, refresh the page prior to testing.

JSON code components defined

NOTE: the screenshots below do not match the JSON Example code.

name: name of Layer within the map service

- index: index of the layer/sub layer as defined within the map service detail

- parent: name of layer within ERT Map’s table of contents, defined as the Layer Title within Layers.

- name (within attrs section): alias of attribute as defined within the Fields section of the Layer within the map service

- attr (within attrs section): name of attribute as defined within the Fields section of the Layer within the map service

- type (within attrs section): indicates search types other than string match.

- noFind - not findable,

- number - numeric range,

- comboAttr - allows two or more attributes to be grouped such that they can be combined differently than the default AND,

- select - dropdown list,

- selectType (within select section): indicates whether the dropdown list will be manually defined (data) or utilize a domain list within the map service (dataquery) or use the selection of one dropdown list to dynamically populate a second dropdown menu (subquery)

- data: used to manually define values within dropdown list values

- size (OPTIONAL): determines the size of the selection list

- exact (OPTIONAL): makes the comparison = instead of like

- val: data value as it appears within the layer's attribute table

- disp: value as it should actually be displayed, as the val is often a code or not user-friendly.

- dataquery: use a domain table published within the map service to define the values within the dropdown list

- queryLayer: same as parent - name of layer within ERT Map’s table of contents, defined as the Layer Title within Layers.

- querySubLayer: index of the domain table (layer/sub layer) as defined within the map service detail

- querySubLayerName: name of domain table (table/layer) within the map service

- outFields: name of attribute within domain table as defined in the map service

- valField: name of field/attribute which contains the display/value attributes to populate the list from a map service query - typically the same as outFields

- dispField: name of field/attribute which contains the display/value attributes to populate the list from a map service query - typically the same as outFields

- subquery: same as dataquery but allows specifying another feature search attribute (queryField) as a name of another field in this layer which when values are selected, a query using only those values will be done against the sub-table’s specified attribute (queryAttr) in order to dynamically populate the field, such as only populating the sub-watersheds intersecting a selected watershed field.

JSON Example

The example text can be downloaded here.

back to top

Related Topics:

Feature Search

- Layers

- Map Service Specifications

Terms & Conditions

This functionality allows users assigned the Administrator Role the ability to:

Edit the Terms & Conditions

- View the Version History

- View Accept Dates which indicates when Users have accepted the various versions of the Terms & Conditions

Edit

From the Admin menu, select Terms & Conditions.

- Within the Terms & Conditions page, edit as desired.

- Click Preview  to preview the changes.

- Click the Save button  to save the edits.

- At the top of the Terms & Conditions page, a message is displayed indicating that the changes have been saved successfully.

back to top

Version History

From the Admin menu, select Terms & Conditions.

- Within the Terms & Conditions page, click the Version History button.

- The text of each version of the Terms & Conditions is displayed along with the Version number and Date Added.

back to top

Accept Dates

From the Admin menu, select Terms & Conditions.

- Within the Terms & Conditions page, click the Accept Dates  button.

- The User ID, Version accepted by the user, and Date Accepted is displayed.

back to top

Configure Settings

Administrators of the system have additional privileges which enable them to configure the USFWS email address. When a project has been submitted with a Final Status and response report of Level 3, the system automatically notifies the USFWS by sending an email to the email address configured here.

Steps:

From the Admin menu, select the Configure Settings option.

- Within the Configure Settings page, enter the email address of the USFWS and click Save Configuration.

Email Templates

This functionality allows users assigned the Administrator Role the ability to view and edit the Email Templates used by the system to email Users regarding a specific project and upon completion of the review process.

Steps:

From the Admin menu, select Email Templates.

- Within the Email Templates page, the two templates are listed.

- project-email-template: email text sent to client upon submitting a project, including the project details;

- review-complete-external: email text sent to client upon completion of project analysis;

- Click the Title to view the template.

- The template is displayed within the Email Templates Details page.

- To edit the template, click the Edit  menu.

- Edit the Subject and/or Body of the email template as desired. NOTE: [node:...] denotes a Token Replacement which will be autopopulated with the appropriate value. A list of the Token Replacements available for use can be found by clicking the link above the Subject.

- Click View Changes to view the edits made to the project.

- Click Preview  to preview the changes.

- Click the Save button  to save the edits.

- At the top of the Email Template Details page, a message is displayed indicating that the Layer has been created successfully.

back to top

Glossary

M

My Term

My definition

Index

A

Account, 7

Add Resource, 9

Address, 63

Analysis Layer Attribute, 103

Analysis Layer Triggers, 106

B

Bookmarks, 65

Build a Query, 34

C

Coordinates, 66

D

Details, 28

Draw/Edit, 45

Dynamic Analysis, 95

F

Feature Search, 13, 20, 117

Filter, 30

Find, 63

G

Generate, 84

I

Identify, 13, 24

Insecure, 17

J

JSON, 117

L

Layers, 13, 26

Log In, 5

M

Make A Map, 37

Map, 9, 37

Map Navigation, 60

Map Services, 17

Measure, 68

N

Notes, 85

P

password, 7

Print, 71

R

Receipt, 84

S

Scale, 66

Snap, 72

Snapping Settings, 72

Spatial, 65

Static Structure, 98

Switch Basemap, 74

T

Test Map Service, 15

Tutorial, 1

U

Users, 76

Z

Zoom, 66

Zoom to Coordinates or Scale, 66